# Short Product Description of Granule Pot- and Pan Washing Machine

# 3 programs with Granules and 3 programs with high-powered water

# Complying with Hygiene guidelines and norms DIN 10512 and NSF/ANSI 3

# Capacity (per hour): 180 GN 1/1

# Capacity per program (pots & pans): 6 x GN 1/1, up to 65 mm depth or up to 12 x small containers, loaded directly into the basket without need for extra accessory

# Operator’s panel placed at eye level

# Basket lift to avoid heavy lifting

- Count-down of remaining time shown in the display during the program

- Led lights alerting when wash cycle is finished

- HACCP log accessed via USB port or the Display

# ______________________________________________________________________________

# Full Product Description of Granule Pot- and Pan Washing Machine

Pass through Granule pot- and pan washing machine with automatic hood. Flexible loading system based on Granule pot washing technology.

Efficient washing of GN (Gastronorm) containers, pots, bowls, saucepans, baking trays and utensils.

- Capacity per hour is 180 GN 1/1.

The powerful mechanical action of the Granule technology eliminates any need for soaking, scrubbing or pre-washing.

Food-safety is secured through a controlled amount of high temperature rinse water, fulfilling the requirements of DIN Norm 10512. The rinse with 6 l of fresh water of 85°C for 40 seconds, ensures a surface temperature of min 72 ºC on the dishware, sanitisation through reaching 3 600 HUE (Heat Units Equivalents, according to NSF/ANSI 3). To ensure the right amount of rinse water, a rinse pump is used.

Unique features

- Eliminates any need for soaking, scrubbing or pre-washing

- Low water consumption, average savings of 70 % compared to manual potwashing

- Low rinse volume, from 4 litres per wash cycle

- Low energy consumption, up to 60 % savings compared to manual potwashing

- Low detergent consumption, up to 60 % savings compared to manual potwashing

- Only 1 m2 space needed for the machine

- Capacity per hour (pots & pans): 180 GN 1/1

- Unique Capacity: 12 x GN 1/6, 1/4, 1/9, per wash cycle (without any extra accessories)

- Complying with Hygiene guidelines and norms DIN 10512 and NSF/ANSI 3

- Operator’s panel placed at eye level

- Basket lift to avoid heavy lifting

- 3 programs with Granules and 3 highly efficient powerful water programs

- Count-down of remaining time shown in the display during the program

Construction material

- Wash cabin including wash tank are made of high-quality stainless steel, EN 1.4301. High level of recyclable materials is used in all parts of the product.

Hygiene / HACCP

- The rinse with 6 l of fresh water of 85 °C for 40 seconds, ensures a surface temperature of min 72ºC on the wash ware. Disinfection conforms to NSF/ANSI 3 (reaching 3600 HUE).

- The rinse with 4 l of fresh water of 85 °C for 20 seconds (ECO Programme), ensures a high surface temperature on the dishware. Disinfection conforms to DIN 10512 standard.

Two integrated systems for hygiene/HACCP and operational data information.

- The final 200 wash cycles could be read out via display;

- Date/Hour

- Type of programme / ECO/Short/Normal

- Washing with Granules is marked with an additional ”G”

- Average temperature in the wash tank during the cycle is marked with e.g. „65“

- Average temperature in the rinse tank during rinsing is marked with e.g. „85“

- “OK“ indicates correct amount of rinse water volume.

- Error codes

- Accumulated values for water and energy consumption

- Possible to download log data via USB port, the latest 200 wash cycles are available.

Built-in intelligence – GD Memo™

- Indication for the operator when it is time to exchange PowerGranules, renew tank wash water or time for periodical service.

Detergent and rinse agent

230 VAC signals available in separate connection box for detergent, rinse agent, dosing equipment and probes.

PowerGranules®

- The machine operates with 8 liter of long-lasting PowerGranules®, made of POM (PolyOxyMethylene copolymer). PowerGranules® are especially developed for GRANULDISK machines.

- One load of long-lasting PowerGranules® are recirculated in the potwasher for in average 2500 wash cycles and can wash as many as up to 15.000 GN 1/1 or equivalent in other pots and pans.

- The material in the PowerGranules® is approved from FDA to be used in contact with food.

| Technical data: |  |
| --- | --- |
| Back flow protection | EN 1717 / return flow protection of type AB with an air gap in accordance with EN 13077. |
| Certifications/Approvals; Company Certification; | Machine manufactured according to the DIN 10512 hygiene guidelines CE ISO 9001: 2015 ISO 14001:2015 |
| Machine dimensions: | 1025 (width) x 957 (depth) x 2079 +/-25 (height with door open) 1736 +/- 25 mm (height with door closed) |
| Weight, when full: | 381 kg |
| Weight, empty: | 257 kg |
| Capacity (pot-wash): | 180 GN 1/1 65 mm per hour. |
| Loading dimensions: | Pot wash rack size max dimensions for loading; basket Ø 700 mm, max loading height 570 mm. |
| Loading volume: | 220 l |
| Wash programmes (pot-wash): | ECO program (with and without Granules) 2 min |
|  | Short program: (with Granules) 3 min (without Granules) 2:30min |
|  | Normal program: (with Granules) 5 min (without Granules) 4:30 min |
| Loading and unloading height: | Approx. 900 mm +/- 25 mm |
| Floor clearance: | 170 ± 25 mm |
| Height clearance (roof): | 2 079 mm |
| Wash water tank: | 108 l |
| Wash water temperature: | 65 °C |
| Rinse water temperature: | 85 ºC |
| Rinse water volume: | 6 l per rinse/cycle in order to comply with the hygiene norm of 3 600 HUE. (NSF/ANSI-3) 4 l per rinse/cycle (ECO Programme) in order to comply with DIN 10512. |
| Hot water consumption, max need during filling: | 15 l/min |
| Water connection: | G 3/4" BSP male (DN 20) |
| Hot water pressure: Cold water pressure: | 1 – 6 bar / at open machine inlet valve 1 – 6 bar / at open machine inlet valve 3 – 6 bar if equipped with optional steam reduction |
| Water hardness: | 3 - 7 °dH |
| Filling and heating time: | approx 40 min (400V/50Hz, cold water connection 10-20 °C) |
| Drain connection: | PEH pipe (polyethylene) – 32 mm |
| Drain time: | approx 5 min |
| Gully: | Capacity required at least 50 litres/minute |
| Granule quantity: | 8 litres |
| Voltage: | 3~ 400/415 V / 50 Hz or 60 Hz + PE 3~ 380 V / 50 Hz or 60 Hz + PE |
| Fuse protection: | 400/415 V: 32 A cold water connection 380 V: 32 A cold water connection |
| Protection enclosure | IPX 5 |
| Max. power: | 11,5 kW |
| Pump motor: | 2,2 kW |
| Tank element: | 9 kW |
| Rinse tank element: | 9 kW |
| Recommended ventilation capacity: | Extraction hood with capacity 500 m3/h. If machine equipped with steam reduction unit (optional) aggregate 200 m3/h, and if equipped with EcoExchanger 100 m³ is enough. |
| Sound pressure level loaded machine operated with Granules: | <70 dB(A) as per ISO 11203 standard |

# ___________________________________________________________________________________