# Short Product Description of Granule Pot- and Pan Washing Machine

# 3 programs with Granules and 3 programs with high-powered water

# Complying with Hygiene guidelines and norms DIN 10512 and NSF/ANSI 3.

# Capacity (per hour): 96 GN 1/1, up to 200 mm depth or 192 GN 1/2, up to 200 mm depth

# Capacity per program (pots & pans): 4 x GN 1/1, up to 200 mm depth or up 8 x GN 1/2 up to 200 mm depth

# Loading in two levels

# Operator’s panel placed at eye level

- Count-down of remaining time shown in the display during the program

- Led lights alerting when wash cycle is finished

# HACCP log accessed via a USB port or the Display

# ______________________________________________________________________________

# Full Product Description of Granule Pot- and Pan Washing Machine

Frontloaded Granule pot- and pan washing machine. Flexible loading system in two levels based on Granule pot washing technology.

Efficient washing of GN (Gastronorm) containers, pots, bowls, saucepans, baking trays and utensils.

- Capacity per hour is 96 GN 1/1 up to 200 mm depth or up to 192 GN 1/2 up to 200 mm depth.

The powerful mechanical action of the Granule technology eliminates any need for soaking, scrubbing or pre-washing.

Food-safety is secured through a controlled amount of high temperature rinse water, fulfilling the requirements of DIN Norm 10512. The rinse with 8 l of fresh water of 85°C for 40 seconds, ensures a surface temperature of min 72ºC on the dishware, sanitisation through reaching 3 600 HUE (Heat Unit Equivalents; according to NSF/ANSI 3).

To ensure the right amount of rinse water, a rinse pump is used.

Unique features

- Eliminates any need for soaking, scrubbing or pre-washing

- Low water consumption, average savings of 70 % compared to manual potwashing

- Low rinse volume, from 4 litres per wash cycle

- Low energy consumption, up to 60 % savings compared to manual potwashing

- Low detergent consumption, up to 60 % savings compared to manual potwashing

- Only 1 m2 space needed for the machine

- Capacity per hour (pots & pans): 96 GN 1/1 up to 200 mm depth

- Unique capacity per cycle: 4 GN 1/1 or 8 GN 1/2 (possible to load without extra accessories)

- Complying with Hygiene guidelines and norms DIN 10512 and NSF/ANSI 3,

- Ergonomic for the Operator, control panel at eye level

- 3 programs with Granules and 3 highly efficient powerful water programs,

- Count-down of remaining program time shown in the display during the program

- Led lights alerting when wash cycle is finished,

- HACCP log accessed via a USB port or the Display

Construction material

- Wash cabin including wash tank are made of high-quality stainless steel, EN 1.4301. High level of recyclable materials is used in all parts of the product.

Hygiene / HACCP

- The rinse with 8 l of fresh water of 85 °C for 40 seconds, ensures a surface temperature of min 72 ºC on the wash ware. Disinfection conforms to NSF/ANSI 3 (reaching 3600 HUE).

- The rinse with 4 l of fresh water of 85 °C for 20 seconds (ECO Programme), ensures a high surface temperature on the dishware. Disinfection conforms to DIN 10512 standard.

Two integrated systems for hygiene/HACCP and operational data information

- The latest 200 wash cycles can be viewed via the display.

- Date/Hour

- Type of programme / ECO/Short/Normal

- Washing with Granules is marked with an additional ”G”

- Average temperature in the wash tank during the cycle is marked with e.g. „65“

- Average temperature in the rinse tank during rinsing is marked with e.g. „85“

- “OK“ indicates correct amount of rinse water volume

- Error codes

- Accumulated values for water and energy consumption

- Possible to download log data via USB port; the latest 200 wash cycles are available.

Built-in intelligence – GD Memo™

- Indication for the operator when it is time to exchange PowerGranules, renew tank wash water or time for periodical service.

Detergent and rinse agent

230 VAC signals available in separate connection box for detergent, rinse agent, dosing equipment and probes.

PowerGranules®

- The machine operates with 6 liters of long-lasting PowerGranules®, made of POM (PolyOxyMethylene copolymer). PowerGranules® are especially developed for GRANULDISK machines.

- One load of long-lasting PowerGranules® are recirculated in the potwasher for in average 2500 wash cycles and can wash as many as up to 15.000 GN 1/1 or equivalent in other pots and pans.

- The material in the PowerGranules® is approved from FDA to be used in contact with food.

| Technical data: |  |
| --- | --- |
| Back flow protection | EN 1717 / return flow protection of type AB with an air gap in accordance with EN 13077. |
| Certifications/Approvals; Company Certification; | Machine manufactured according to the DIN 10512 hygiene guidelines CE ISO 9001: 2015 ISO 14001:2015 |
| Machine dimensions: | 845 (width) x 965 (depth) x 1770+/-25 (height) mm |
| Weight, filled: | 372 kg |
| Weight, empty: | 278 kg |
| Capacity: (pot-wash) | Capacity 96 GN 1/1 up to 200 mm depth. |
| Loading dimensions: | Pots up to the maximum rack dimensions; Ø 500 mm with 650 mm depth – or equivalent in other utensils. |
| Loading volume: | 205 l |
| Wash programmes (pot-wash): | ECO program: (with and without Granules) 2:30 min |
|  | Short program: (with Granules) 4:40 min, without Granules 3:40 min |
|  | Normal program: (with Granules) 6:40 min, without Granules 5:40 min *if steam reduction unit is turned on, one extra minute to be added to short and normal programme. |
| Floor clearance: | 170 ± 25 mm |
| Height clearance (roof): | 1780 mm |
| Wash water tank: | 84 litres |
| Wash water temperature: | 65 °C |
| Rinse water volume: | 8 l per rinse/cycle in order to comply with the hygiene norm of NSF/ANSI-3 4 l per rinse/cycle (ECO Programme) in order to comply with DIN 10512. |
| Rinse water temperature: | 85 °C |
| Hot water consumption, max need during filling: | 15 l/min |
| Water connection; | G 3/4" BSP male (DN 20) |
| Hot water pressure; Cold water pressure: | 1 – 6 bar / at open machine inlet valve 3 – 6 bar / at open machine inlet valve* *3 – 6 bar for cold water is required if using the equipped steam reduction unit and for the Granule valve to open and close. |
| Water hardness: | 3-7 °dH |
| Filling and heating time: | approx 15 min (25A connected to hot water supply 55-65°C) |
| Drain connection: | PEH pipe (polyethylene) – 32 mm |
| Drain time: | approx 5 min |
| Gully: | Capacity required at least 50 litres/minute |
| Granule quantity: | 6 litres |
| Voltage: | 3~ 400 V/50 Hz or 60Hz + PE 3~ 208 V/60 Hz + PE 3~ 230 V/50 or 60 Hz + PE 3~ 380 V/50 or 60 Hz + PE 3~ 415 V/50 Hz + PE 3~ 440 V/60 Hz + PE |
| Fuse protection: | 400 V: 25 A hot water connection 208 V: 50 A hot water connection 230 V: 40 A hot water connection 380 V: 25 A hot water connection 415 V: 25 A hot water connection 440 V: 25 A hot water connection |
| Enclosure rating | IPX5 |
| Max. power: | 12,3 kW |
| Pump motor: | 3 kW |
| Tank element: | 9 kW |
| Rinse tank element: | 9 kW |
| Recommended ventilation capacity: | Extraction hood with capacity 400 m3/h. If machine equipped with steam reduction unit (Optional) aggregate 150 m3/h. |
| Sound pressure level loaded machine operated with Granules: | < 70 dB(A) |

# ___________________________________________________________________________________